## Slide 1: Project report
Happy Greens. Mikhail Stukalo

## Slide 2: Project from Idea to Implementation
Build an ML algorithm that predicts hit or miss for golf putting
  The algorithm can be used to improve putting skills
  Potentially, can be further developed into an AR app for “playing” golf using a phone and a club
Final implementation includes:
  Prediction algorithm based on CatBoost classifier that assesses the probability of a successful hit
  A Python app (currently running under Linux only) that analyzes a putt and makes a prediction
If only I had an app like this …

## Slide 3: Project pipeline plan
Week 1
Week 2
Week 3
Week 4
Week 5
You are here
Collect all equipment
Finish all tutorials
Come up with the data collection protocol
Code data collection software
Assemble the device
Collect ≈ 30 samples
Test data cleaning
Collect 180-240 samples
Clean the data
Create classification algorithm using Logistic, SVM, CatBoost
Create a Python app for “online” data collection and prediction using the model
Write-up the project
Chose that one

## Slide 4: Week-by-week Progress
Week 1-2
Week 3
Week 4
ST-Link Sensor kit, NUCLEO, Pi 3+, … golf equipment
Tutorials
Assembling the sensor
Developing data collection software (Pi)
Collecting samples
Data cleaning (putt detection)
Feature extraction
Modelling
Prototyping
Write-up
Submitting the project

## Slide 5: Data Transmission
Sampling rate: 30 ms (?). Probably should have made it more granular
Fields: Timestamp, Acc_X, Acc_Y, Acc_Z, Gyr_X, Gyr_Y, Gyr_Z
GATT
Python client:
Bluepy
Bluez
Variables
Dataset
Features
Model
Distance
Prediction
True response

## Slide 6: Data Collection
Balanced dataset of 250 observations

## Slide 7: State Machine
Start
Back
Forward
Stop
State features:
Slight increase in Acc-Z
Action:
Record start of the putt
State features:
Monotonically decreasing Z-axis
Action:
Use for a ‘helper’ model
State features:
Monotonically increasing Z-axis until maximum
Action:
Store accelerometer and gyro for the model
State features:
Maximum Acc-Z reached
Action:
Expect start
Accelerometer Z-axis

## Slide 8: Putt detection
Find break though the threshold (1)
Move window left by prespecified margin (25 observations) and find local maximum (2)
Create prespecified window (100 observations) and find local maximum (3)
Find local minimum between (2) and (3)
Threshold
(1)
(2)
Left margin
(3)
(4)
Putt-detection algorithm
Marked dataset of 30 putts

## Slide 9: Model design
Raw inputs
Inputs (Stage 3) offset:
Distance
Gyro (X,Y,Z)
Acc (X,Y,Z)
True response (1/0)
Putt forward
For Acc and Gyro
Range
Min, Max, Last
Mean, StDev
Mean StDev of recentered
Vector size
Slope
Feature selection
Exclude
Based on experiments with feature selection
X-axis for Axx and Gyro
Vector size
Model
Output
1 (hit) / 0 (miss)
Split
Train/validation/test split
- 30/70% test/train (75/175 observations)
- Train is split 30/70 to validation and train (53/122 observations)

## Slide 10: Catboost Precision
Validation set (53 observations)
Test set (75 observations)

## Slide 11: Feature Importance
Top-10 Features

## Slide 12: Working prototype
https://youtu.be/--KsTxibZ40

## Slide 13: Possible improvements
Collect more data
  With the current number of features (37) and observations (122 in train set), overfitting is a big problem
Make data more granular (probably 10ms or less)
  Because of low resolution of the data, we have to rely on having many features in the hope to distinguish between successful and unsuccessful putts
Increase the range and granularity of distances

## Slide 14: Full Video
https://youtu.be/2S7rDOkyQkU

## Slide 15: Unrelated: What to do with Raspberry Pi